## Slide 1: Overview and Rationale for Modelica Stream Connectors January 27, 2009
Revisions:
May 25, 2008 | by Martin Otter (DLR). First version. Presented at 57th Modelica Design Meeting
June 9, 2008 | by Martin Otter (DLR): Considerably improved version. Presented at EUROSYSLIB WP5.3 meeting
June 11, 2008 | by Martin Otter (DLR): Newly structured and considerably improved (after EUROSYSLIB meeting)
Jan. 27, 2009 | by Francesco Casella (Politecnico di Milano): Updated with changes in the final Modelica_Fluid release 1.0
Notes: <number>

## Slide 2: Contents
Overview and Rationale for Stream Connectors - Page <number>
Part A Overview
1. Stream Variables and Stream Operators
2. Modeling with Streams
Part B Rationale
3. Basic Problems of Fluid Connectors
4. Stream Connection Semantics
5. Reliable Handling of Ideal Mixing
6. Open Issues
7. Status
8. History and Contributors

## Slide 3: Part A Overview
Overview and Rationale for Stream Connectors - Page <number>
At the 57th Modelica design meeting (May 25-28, 2008) a new fundamental type of connector variables "stream" was introduced for the next Modelica Language Specification Version 3.1, because the two standard types of port variables used in all component oriented modeling systems
potential/flow, across/through, effort/flow variables
are not sufficient to model flow of matter in a reliable way.
Modelica_Fluid 1.0 is based on this new concept.
These slides give an introduction in to this new connector type and provide a rationale why it is introduced and the benefits of the concept.

## Slide 4: 1. Stream Variables and Stream Operators
Overview and Rationale for Stream Connectors - Page <number>
Purpose
Reliable handling of convective mass and energy transport in thermo-fluid systems with bi-directional flow of matter.
Relevant boundary conditions and balance equations are fulfilled in a connection point.
mass and energy balance fulfilled in the idealized connection point
(convective) transport of matter

## Slide 5
Overview and Rationale for Stream Connectors - Page <number>
Examples of an interface for fluid components
p | absolute pressure | potential variable
m_flow | mass flow rate | flow variable (describes transport of matter)
h | specific enthalpy | stream variable (quantity transported with matter)
Xi | mass fraction | stream variable (quantity transported with matter)
A stream variable hi of a connector i is associated with
a flow variable m_flow ("0 = Σ m_flowi") and
a stream balance equation ("0 = Σ m_flowi*<upstream value of hi>")
{

## Slide 6
Overview and Rationale for Stream Connectors - Page <number>
 | value of stream variable hi in connector i
hi | if flow from component to connection point (m_flowi ≤ 0)
inStream(hi) | if flow from connection point to component (m_flowi > 0
actualStream(hi) | for both flow directions (= if m_flowi > 0 then instream(hi) else hi) only to be used when absolutely necessary(!)
Reliable handling of bi-directional flow:
h3
inStream(h3)
h2
inStream(h2)
h1
inStream(h1)
(mixing value for m_flowi > 0)

## Slide 7
Overview and Rationale for Stream Connectors - Page <number>
h1
h2
h3
h4
h5
h6
inStream(h1) = h2 = inStream(h3) = h4 = inStream(h5) = h6 inStream(h6) = h5 = inStream(h4) = h3 = inStream(h2) = h1
inStream(h2)
inStream(h3)
inStream(h5)
inStream(h4)
inStream(h1)
inStream(h6)
volume
pressure drop
pressure drop
volume
Energy balance in volume 1:
der(U1) = m_flow1*actualStream(h1) = m_flow1*(if m_flow1 > 0 then inStream(h1) else h1) = m_flow1*(if m_flow1 > 0 then h6 else h1)
Example of a volume – pressure drop network

## Slide 8: 2. Modeling with Streams
Overview and Rationale for Stream Connectors - Page <number>
connector FluidPort SI = Modelica.SIunits;
SI.AbsolutePressure p "Pressure in connection";
flow SI.MassFlowRate m_flow "Mass flow rate";
stream SI.SpecificEnthalpy h_outflow "h if m_flow <= 0";
stream SI.MassFraction X_outflow[nX] "X if m_flow <= 0";
end FluidPort;
Modeling with stream variables is very simple (see following examples)!
For notational convenience, the equations for the mass fractions X
are not shown in the following examples.
Connector definition:
If a connector has one or more stream variables, exactly one (scalar) flow
variable must be present which is the flow associated with all stream variables.

## Slide 9
Overview and Rationale for Stream Connectors - Page <number>
model MixingVolume "Volume that mixes two flows"
replaceable package Medium = Modelica.Media.Interfaces.PartialMedium;
FluidPort port_a, port_b;
parameter Modelica.SIunits.Volume V "Volume of device";
Modelica.SIunits.Mass m "Mass in device";
Modelica.SIunits.Energy U "Inner energy in device";
Medium.BaseProperties medium(preferredMediumStates=true);
equation
// Definition of port variables
port_a.p = medium.p;
port_b.p = medium.p;
port_a.h_outflow = medium.h;
port_b.h_outflow = medium.h;
// Mass and energy balance
m = V*medium.d;
U = m*medium.u;
der(m) = port_a.m_flow + port_b.m_flow;
der(U) = port_a.m_flow*actualStream(port_a.h_outflow) +
port_b.m_flow*actualStream(port_b.h_outflow);
end MixingVolume;
Example: Mixing Volume

## Slide 10
Overview and Rationale for Stream Connectors - Page <number>
model IsenthalpicFlow "No energy storage/losses, e.g. pressure drop, valve, ..."
replaceable package Medium=Modelica.Media.Interfaces.PartialMedium;
FluidPort port_a, port_b:
Medium.ThermodynamicState port_a_state_inflow "State at port_a if inflowing";
Medium.ThermodynamicState port_b_state_inflow "State at port_b if inflowing";
equation
// Medium states for inflowing fluid
port_a_state_inflow = Medium.setState_phX(port_a.p,
inStream(port_a.h_outflow));
port_b_state_inflow = Medium.setState_phX(port_b.p,
inStream(port_b.h_outflow));
// Mass balance
0 = port_a.m_flow + port_b.m_flow;
// Instantaneous propagation of enthalpy flow between the ports with
// isenthalpic state transformation (no storage and no loss of energy)
port_a.h_outflow = inStream(port_b.h_outflow);
port_b.h_outflow = inStream(port_a.h_outflow);
// (Regularized) Momentum balance
port_a.m_flow = f(port_a.p, port_b.p, Medium.density(port_a_state_inflow),
Medium.density(port_b_state_inflow));
end IsenthalpicFlow;
Example: Isenthalpic fluid transport

## Slide 11
Overview and Rationale for Stream Connectors - Page <number>
model IsenthalpicFlow "No energy storage, e.g. pump, heat losses, ..."
replaceable package Medium = Modelica.Media.Interfaces.PartialMedium;
FluidPort port_a, port_b:
Medium.ThermodynamicState port_a_state_inflow "State at port_a if inflowing";
Medium.ThermodynamicState port_b_state_inflow "State at port_b if inflowing";
Modelica.SIunit.Power P_ext "Energy flow via other connectors"
equation
// Medium states for inflowing fluid
port_a_state_inflow = Medium.setState_phX(port_a.p, inStream(port_a.h_outflow));
port_b_state_inflow = Medium.setState_phX(port_b.p, inStream(port_b.h_outflow));
// Mass balance
0 = port_a.m_flow + port_b.m_flow;
// Instantaneous propagation of enthalpy flow between the ports with
// isentropic state transformation
port_a.h_outflow = Medium.isentropicEnthalpy(port_a.p,inStream(port_b.h_outflow));
port_b.h_outflow = Medium.isentropicEnthalpy(port_b.p,inStream(port_a.h_outflow));
// Energy balanced to compute energy flow exchanged with other ports
0 = P_ext + port_a.m_flow*actualStream(port_a.h_outflow)
+ port_b.m_flow*actualStream(port_b.h_outflow);
// (Regularized) Momentum balance
port_a.m_flow = f(port_a.p, port_b.p, Medium.density(port_a_state_inflow),
Medium.density(port_b_state_inflow));
end IsenthalpicFlow;
Example: Isentropic fluid transport

## Slide 12
Overview and Rationale for Stream Connectors - Page <number>
model TemperatureSensor "Ideal temperature sensor"
replaceable package Medium = Modelica.Media.Interfaces.PartialMedium;
FluidPort port(m_flow(min=0)); // No flow out of sensor ever
Modelica.Blocks.Interfaces.RealOutput T "Upstream temperature";
equation
T = Medium.temperature(Medium.setState_phX(port.p, inStream(port.h_outflow));
port.m_flow = 0;
port.h_outflow = Medium.specificEnthalpy(Medium.setState_pTX( Medium.reference_p, Medium.reference_T)); // This value will never be used, since m_flow(min=0), // but it will show up in the plot window.
end TemperatureSensor;
Example: Temperature sensor
Setting "m_flow.min=0" is very important, in order that the temperature sensor has no influence on the stream that it measures, if all mass flow rates are zero; since then
"max(-port.m_flow,ε) = 0" in the inStream(..)-operators of the connected ports!!!

## Slide 13
Overview and Rationale for Stream Connectors - Page <number>
model FixedBoundary_pT "Infinite reservoir with fixed pressure and temperature"
replaceable package Medium = Modelica.Media.Interfaces.PartialMedium;
FluidPort port;
parameter Medium.AbsolutePressure p "Boundary pressure";
parameter Medium.Temperature T "Boundary temperature";
equation
port.p = p;
port.h_outflow = Medium.specificEnthalpy(Medium.setState_pTX(p, T));
end FixedBoundary_pT;
Example: Infinite Reservoir

## Slide 14: Part B Rationale
Overview and Rationale for Stream Connectors - Page <number>
provide a rationale, why reliable bi-directional flow modeling requires a third type of connector variable (streams),
discusses details of the connection semantics of streams,
shows why stream connectors lead to reliable models.
The following slides

## Slide 15: 3. Basic Problems of Fluid Connectors
Overview and Rationale for Stream Connectors - Page <number>
connector FluidPort
import SI = Modelica.SIunits;
SI.AbsolutePressure p "Pressure in connection point";
flow SI.MassFlowRate m_flow "Mass flow rate";
stream SI.SpecificEnthalpy h "Specific enthalpy";
end FluidPort;
Desired connector for bi-directional flow of matter. The intensive quantities transported with the matter (like h) have the newly introduced "stream" prefix:
Observation
This is the most simplest connector description form for the desired class of models (independently how the connected components are described, e.g. lumped, discretized PDE, PDE, ...). It is very unlikely that a "simpler" connector exists.
Goal
Define connection semantic of stream variables, so that the balance equations for stream variables in an infinitesimal small connection point are fulfilled and the equations can be solved reliably.
Notes: <number>

## Slide 16
Overview and Rationale for Stream Connectors - Page <number>
Central Question: What is the meaning of a stream variable, such as "h"?
Balance equations of stream variables for 3 connected components (independently how the components are described, e.g. lumped, PDE, ...)
m1.h
m2.h
m3.h
h_mix
(1) 0 = m1.m_flow*(if m1.m_flow > 0 then h_mix else m1.h) +
m2.m_flow*(if m2.m_flow > 0 then h_mix else m2.h) +
m3.m_flow*(if m3.m_flow > 0 then h_mix else m3.h)
(2) 0 = m1.m_flow + m2.m_flow + m3.m_flow
From the balance equations, it seems natural that the stream variables are one of the occurring variables, e.g., h_mix or m1.h
m1.m_flow
Notes: <number>

## Slide 17
Overview and Rationale for Stream Connectors - Page <number>
but: then, the result will be of the form:
h_mix = if m1.m_flow > 0 then ... else ... m1.h = if m1.m_flow > 0 then ... else ...
e.g. for 2 connected components:
h_mix = if m1.m_flow > 0 then m2.h else m1.h
this means that m1,h, m2.h, h_mix etc. are computed by equations that contain if-clauses which depend on the mass flow rate.
If algebraic systems of equations occur (due to initialization, or ideal mixing, or pressure drop components directly connected together etc.), then these equation systems, inevitably, have unknowns that depend on the unknown mass flow direction, i.e., nasty non-linear equation systems occur that are difficult to solve (since Boolean unknowns as iteration variables)!!!
Notes: <number>

## Slide 18
Overview and Rationale for Stream Connectors - Page <number>
The issue appears even in the most simple case of
MixingVolume – PressureDrop – MixingVolume
connection, if the mass flow rate in the pressure drop does not only depend on pressure, but also on density as a function of the medium state:
h1,p1
mixing volume
mixing volume
h2,p1
h3,p4
h4,p4
m_flow
h2 = if m_flow > 0 then h4 else h1
h3 = h2; // !!!!!
d2 = f1(p1,h2) // density
d3 = f1(p4,h3)
m_flow = f2(p1, p4, d2, d3)
Note: Even for the most simplest case (volume – pressure drop – volume), a nasty non-linear equation system appears, since m_flow = f2(..., m_flow > 0); Can sometimes be fixed by replacing "m_flow > 0" with "p4 - p1 > 0"
pressure drop
Notes: <number>

## Slide 19
Overview and Rationale for Stream Connectors - Page <number>
Major problem:
Independently of the flow direction: h3 = h2
m_flow > 0: m_flow = f2(..., d2(p1,h4), d3(p4,h4)); m_flow < 0: m_flow = f2(..., d2(p1,h1), d3(p4,h1));
However (see next slides): f2(..) must be a function of d2(p1,h1), d3(p1,h4) !!!
h1,p1
mixing volume
mixing volume
h2,p1
h3,p4
h4,p4
m_flow
h2 = if m_flow > 0 then h4 else h1
h3 = h2; // !!!!!
d2 = f1(p1,h2) // density
d3 = f1(p4,h3)
m_flow = f2(p1, p4, d2, d3)
pressure drop
Additionally, every pressure drop component is not differentiable at m_flow = 0. If non-linear equation systems occur, then this system is not differentiable at a critical point, and then every non-linear solver has difficulties.
Notes: <number>

## Slide 20
Overview and Rationale for Stream Connectors - Page <number>
When m_flow > 0, dp > 0: The "blue" curve (m_flow1) is computed. When m_flow < 0, dp < 0: The "red" curve (m_flow2) is computed.
When m_flow changes from positive to negative, the interpolation jumps from curve "blue" to "red". This means, that m_flow is not differentiable at m_flow = 0.
If m_flow appears in a non-linear equation system, this is not good, because the pre-requisite of a non-linear solver is not fulfilled in the critical point at m_flow = 0!!!!
d(p1,h1)
d(p1,h4)

## Slide 21
Overview and Rationale for Stream Connectors - Page <number>
Correct treatment: m_flow = f2(..) is a function of d2(p1,h1), d3(p1,h4) !!!
In order that the correct f2(..) function is used ("green" curve), the "density" of the "actual" flow (m_flow > 0) and the "density" of the "reversed flow" (m_flow < 0) are needed at the same time instant. Only then, regularization around m_flow = 0 is possible, leading to a smooth characteristic.
d(p1,h1)
d(p1,h4)

## Slide 22
Overview and Rationale for Stream Connectors - Page <number>
Note, the only way to avoid the identified problems is to not compute h_mix, m1.h, etc. Instead:
d2_outflow = f1(p1,h4) // flow from h4 to h1
d3_outflow = f1(p4,h1) // flow from h1 to h4
m_flow = f2(p1, p4, d2_outflow, d3_outflow)
h1,p1
mixing volume
mixing volume
h2,p1
h3,p4
h4,p4
m_flow
pressure drop
Summary: It is impossible to arrive at reliable, bi-directional flow models, if the actual
intensive quantities (like h_mix, h1, h2, ...) are used in the connector equations.
Notes: <number>

## Slide 23: 4. Stream Connection Semantics
Overview and Rationale for Stream Connectors - Page <number>
port_a.h_outflow
inStream(port_a.h_outflow)
port_a.h_outflow
inStream(port_b.h_outflow)
Central idea:
compute value for "outflow" and
inquire value for "inflow" with operator "inStream(..)"
instream(port_a.h_outflow
port_b.h_outflow
Notes: <number>

## Slide 24
Overview and Rationale for Stream Connectors - Page <number>
connector FluidPort
SI = Modelica.SIunits;
SI.AbsolutePressure p "Pressure in connection point";
flow SI.MassFlowRate m_flow "Mass flow rate";
stream SI.SpecificEnthalpy h_outflow "h close to port if m_flow < 0";
end FluidPort;
pipe1.port_a.m_flow
connect(pipe1.port_a, pipe2.port_b); connect(pipe1.port_a, pipe3.port_b);
pipe1.port_a.p = pipe2.port_a.p pipe1.port_a.p = pipe3.port_a.p 0 = pipe1.port_a.m_flow + pipe2.port_a.m_flow + pipe3.port_a.m_flow
pipe2.port_a.m_flow
pipe3.port_a.m_flow
pipe1.port_a.h_outflow
No connection equations are generated for stream variables (!)
Basic connector definition
Notes: <number>

## Slide 25
Overview and Rationale for Stream Connectors - Page <number>
(1) 0 = m1.c.m_flow*(if m1.c.m_flow > 0 then h_mix else m1.c.h_outflow) +
m2.c.m_flow*(if m2.c.m_flow > 0 then h_mix else m2.c.h_outflow) +
m3.c.m_flow*(if m3.c.m_flow > 0 then h_mix else m3.c.h_outflow)
(2) 0 = m1.c.m_flow + m2.c.m_flow + m3.c.m_flow
model : m1,m2,m3; connector: c; flow : m_flow stream : h_outflow
balance equations
m1
m2
m3
h_mix (h for ideal mixing)
c.h_outflow
(1) 0 = max(m1.c.m_flow,0)*h_mix - max(-m1.c.m_flow,0)*m1.c.h_outflow +
max(m2.c.m_flow,0)*h_mix – max(-m2.c.m_flow,0)*m2.c.h_outflow +
max(m3.c.m_flow,0)*h_mix – max(-m3.c.m_flow,0)*m3.c.h_outflow
(2) 0 = max( m1.c.m_flow,0) + max( m2.c.m_flow,0) + max(m3.c.m_flow,0)
- max(-m1.c.m_flow,0) – max(-m2.c.m_flow,0) – max(m3.c.m_flow,0)
(3) h_mix = (max(-m1.c.m_flow,0)*m1.c.h_outflow + max(-m2.c.m_flow,0)*m2.c.h_outflow + max(-m3.c.m_flow,0)*m3.c.h_outflow) / (max(m1.c.m_flow,0) + max(m2.c.m_flow,0) + max(m3.c.m_flow,0))
(4) h_mix = (max(-m1.c.m_flow,0)*m1.c.h_outflow +
max(-m2.c.m_flow,0)*m2.c.h_outflow +
max(-m3.c.m_flow,0)*m3.c.h_outflow) /
(max(-m1.c.m_flow,0) + max(-m2.c.m_flow,0) + max(-m3.c.m_flow,0))
mass balance
Notes: <number>

## Slide 26
Overview and Rationale for Stream Connectors - Page <number>
(4) h_mix = (max(-m1.c.m_flow,0)*m1.c.h_outflow +
max(-m2.c.m_flow,0)*m2.c.h_outflow +
max(-m3.c.m_flow,0)*m3.c.h_outflow) /
(max(-m1.c.m_flow,0) + max(-m2.c.m_flow,0) + max(-m3.c.m_flow,0))
Definition:
inStream(m1.c.h_outflow) = h_mix for m1.c.m_flow > 0
Reason: This definition prepares for the changing flow direction at m1.c.m_flow = 0: If only m1.c.m_flow is changing the flow direction, then h_mix is discontinuous at m1.c.m_flow = 0.
However, h_mix for m1.c.m_flow > 0 is continuous at m1.c.m_flow = 0
since m1.c.h_outflow does not appear in the equation, because for
inflowing flow, this variable does not influence the mixing and the same formula is used also for the reversed direction!!!
Notes: <number>

## Slide 27
Overview and Rationale for Stream Connectors - Page <number>
(4) h_mix = (max(-m1.c.m_flow,0)*m1.c.h_outflow +
max(-m2.c.m_flow,0)*m2.c.h_outflow +
max(-m3.c.m_flow,0)*m3.c.h_outflow) /
(max(-m1.c.m_flow,0) + max(-m2.c.m_flow,0) + max(-m3.c.m_flow,0))
inStream(m1.c.h_outflow) = h_mix for m1.c.m_flow > 0
Definition:
(5) inStream(m1.c.h_outflow) = (max(-m2.c.m_flow,0)*m2.c.h_outflow +
max(-m3.c.m_flow,0)*m3.c.h_outflow) /
(max(-m2.c.m_flow,0) + max(-m3.c.m_flow, 0))
≈ (max(-m2.c.m_flow,ε)*m2.c.h_outflow +
max(-m3.c.m_flow,ε)*m3.c.h_outflow) /
(max(-m2.c.m_flow,ε) + max(-m3.c.m_flow,ε))
For 2 connections:
(6) inStream(m1.c.h_outflow) = (max(-m2.c.m_flow,0)*m2.c.h_outflow /
max(-m2.c.m_flow,0)
= m2.c.h_outflow
For 3 connections with m3.c.m_flow.min=0 (One-Port Sensor):
(7) inStream(m1.c.h_outflow) = m2.c.h_outflow
(8) inSteram(m3.c.h_outflow) = (max(-m1.c.m_flow,0)*m1.c.h_outflow +
max(-m2.c.m_flow,0)*m2.c.h_outflow) /
(max(-m1.c.m_flow,0) + max(-m2.c.m_flow, 0))
Notes: <number>

## Slide 28
Overview and Rationale for Stream Connectors - Page <number>
If all mass flow rates are zero, the stream balance equation is identically fulfilled, independently of the values of h_mix, and mi.c.h_outflow. Therefore, there are an infinite number of solutions.
(5) inStream(m1.c.h_outflow) = (max(-m2.c.m_flow,0)*m2.c.h_outflow +
max(-m3.c.m_flow,0)*m3.c.h_outflow) /
(max(-m2.c.m_flow,0) + max(-m3.c.m_flow, 0))
≈ (max(-m2.c.m_flow,ε)*m2.c.h_outflow +
max(-m3.c.m_flow,ε)*m3.c.h_outflow) /
(max(-m2.c.m_flow,ε) + max(-m3.c.m_flow,ε))
The basic idea is to approximate the "max(..)" function to avoid this case:
Then a unique solution of this equation always exists.
If all mass flow rates are identically to zero, the result is the mean value of
the involved specific enthalpies:
(6) inStream(m1.c.h_outflow) ≈ (max(-m2.c.m_flow,ε)*m2.c.h_outflow +
max(-m3.c.m_flow,ε)*m3.c.h_outflow) /
(max(-m2.c.m_flow,ε) + max(-m3.c.m_flow,ε))
= (ε*m2.c.h_outflow + ε*m3.c.h_outflow) / (ε + ε) = (m2.c.h_outflow + m3.c.h_outflow) / 2

## Slide 29
Overview and Rationale for Stream Connectors - Page <number>
// Actual regularization for small mass flow rates
// Determine denominator s for exact computation
s := sum( max(-mj.c.m_flow,0) )
// Define a "small number" eps (nominal(v) is the nominal value of v)
eps := relativeTolerance*min(nominal(mj.c.m_flow))
// Define a smooth curve, such that alpha(s>=eps)=1 and alpha(s<=0)=0 // (using a polynomial of 3rd order)
alpha := smooth(1, if s > eps then 1 else
if s > 0 then (s/eps)^2*(3-2*(s/eps)) else 0);
// Define function positiveMax(v) as a linear combination of max(v,0) // and of eps along alpha
positiveMax(-mj.c.m_flow) := alpha*max(-mj.c.m_flow,0) + (1-alpha)*eps;
// Use "positiveMax(..)" instead of "max(.., eps)" in the // inStream(..) definition!
an approximation is only used, if all mass flow rates are small,
the characteristic is continuous and differentiable (max(.., ε) is continuous but not differentiable)
The actual regularization is a bit more involved, in order that

## Slide 30: 5. Reliable Handling of Ideal Mixing
Overview and Rationale for Stream Connectors - Page <number>
"DryAirNasa" (ideal gas with f(p,T)) and "FlueGasSixComponents" (mixture of ideal gases with 6 substances)
Detailed pipe friction correlations for the laminar and turbulent flow regimes
Ideal mixing point (no volume) in the connection point.
reference problem
All the details are described in a report from M. Sielemann and M. Otter. Only the major results are presented on the following slides.

## Slide 31
Overview and Rationale for Stream Connectors - Page <number>
22 | Modelica_Fluid (previous version; non-smooth iteration variables; no sim.)
6 | ThermoPower (non-smooth iteration variables)
3 | Modelica_Fluid (new version with "stream"; smooth iteration variables)
Number of iteration variables for "FlueGasSixComponents" (mixture of ideal gases with 6 substances)
(Note: with a volume in the connection point there would be 2+6=8 state variables, i.e., an implicit DAE solver would have 8 iteration variables).

## Slide 32
Overview and Rationale for Stream Connectors - Page <number>
replaceable package Medium = Modelica.Media.Interfaces.PartialMedium; Medium.BaseProperties medium_a_inflow; Medium.BaseProperties medium_b_inflow; equation medium_a_inflow.p = port_a.p; medium_b_inflow.p = port_b.p; medium_a_inflow.h = inStream(port_a.h_outflow); medium_b_inflow.h = inStream(port_b.h_outflow); port_a.h_inflow = medium_a_inflow.h; port_b.h_inflow = medium_b_inflow.h; port_a_d_inflow = medium_a_inflow_d; port_b_d_inflow = medium_b_inflow_d;;
Basic (previous) form of "pressure drop" component:
If medium is not f(p.h), a non-linear equation system appears, in order to compute medium_a_inflow.h from medium_a_inflow.T (and from the pressure). For an ideal mixing point (or any other non-linear equation system), a tool will therefore select T as iteration variable.

## Slide 33
Overview and Rationale for Stream Connectors - Page <number>
Severe disadvantage: Temperature is discontinuous and therefore the iteration variable is discontinuous!!!
T as iteration variable (discontinuous) -> at m_flow = 0, jump in iteration variable; every non-linear solver has difficulties with this.
m_flow as iteration variable (continuous)

## Slide 34
Overview and Rationale for Stream Connectors - Page <number>
replaceable package Medium = Modelica.Media.Interfaces.PartialMedium; equation port_a.h_outflow = inStream(port_b.h_outflow); port_b.h_outflow = inStream(port_a.h_outflow);
port_a_state_inflow = Medium.setState_phX( port_a.p, inStream(port_a.h_outflow),...);
port_b_state_inflow = Medium.setState_phX( port_b.p, inStream(port_b.h_outflow),...); port_a_inflow = Medium.density(port_a_state_inflow); port_b_inflow = Medium.density(port_b_state_inflow);
New form of "pressure drop" component:
If medium is not f(p.h), no (explicit) non-linear equation system appears, since the medium state is computed from the known port properties.
However, the function "setState_phX" solves internally a non-linear equation system (with Brents algorithm; a fast and very reliable algorithm to solve one non-linear algebraic equation in one unknown).

## Slide 35
Overview and Rationale for Stream Connectors - Page <number>
A tool can now compute all variables in a point with N connections from
N-1 mass flow rates and 1 pressure
in an explicit forward sequence and therefore selects these variables as iteration variables (and these variables are always continuous):
The N-th mass flow rate is computed from the mass balance
The port-specific mixing enthalpies (h_mix(m_flow_i = 0)) can be computed, since they depend only on known variables (enthalpies in the volumes and the mass flow rates).
The medium states can be computed via Medium.setState_phX(..), since p,h,X are known now.
All medium properties can be computed from the medium state, especially the density.
Via the momentum balance, the mass flow rates can be computed (= residue equations).
Analysis does also hold for initialization: With this approach, initialization will work much better, since mass flow rates are selected as iteration variables. A default start value of zero for mass flow rates is often sufficient for the solver.

## Slide 36
Overview and Rationale for Stream Connectors - Page <number>
Summary
If the "streams" concept is used, and the pressure drop components are implemented as sketched in the previous slide, then an ideal mixing point with N connections gives rise to a non-linear system of algebraic equations (if N > 2 and no min-attributes are set) that has the following properties:
The number of iteration variables is N (independent of the medium, and how many substances are in the medium).
The iteration variables are continuous everywhere (since as iteration variables, N-1 mass flow rates and one pressure is used).
The iteration variables are in most cases differentiable (due to the definition of stream-variables and of the inStream(..) operator). The iteration variables are not differentiable, if all mass flow rates in an ideal mixing point become zero at the same time instant. If this is not the case, they are differentiable.
Default start values of zero for the mass flow rates and for the pressure drop in the pressure drop components, are good guess values for the iteration variables (independent of the medium).
It can therefore be expected that a solution of the equation system is easy to compute by every reasonable non-linear equation solver.

## Slide 37: 6. Open Issues
Overview and Rationale for Stream Connectors - Page <number>
For a regular network of the usual "Volume – Pressure Drop – Volume" structure a non-linear algebraic equation in one unknown is present for every connector of a pressure drop component, if the medium states are not p,h,X. It seems possible to remove all these equation systems by clever symbolic analysis. This issue is not critical, because these scalar implicit equations can be solved reliably. The only issue is to enhance efficiency.
If components from discretized PDEs are connected together, there are two options with respect to the mathematical structure.
One option is to split the momentum balance between two components in two parts, leading to two half-momentum-balances on either side of the connection. This results in one non-linear algebraic equation in one unknown (the pressure) for every connection point, which can be numerically troublesome, expecially at initialization.
The other option is to split the mass and energy balances in two parts, leading to two half-mass-balances on either side of the connection. This results in a high-index problem. If the tool can handle the index reduction, the resulting equations can be solved reliably
Both options are available in the DistributedPipe model of Modelica_Fluid

## Slide 38: 7. Status
Overview and Rationale for Stream Connectors - Page <number>
Detailed specification text for Modelica 3.1 available
(Positive) voting for the specification text for inclusion in Modelica 3.1
Fully functional implementation in Dymola available (version 7.1 and later)
Work going on to implement the concept in OpenModelica and MathModelica
Final release of Modelica_Fluid library v.1.0 changed to new connector design
Detailed tests with sandbox libraries by Rüdiger Franke and Michael Sielemann
All examples of Modelica_Fluid simulate without problems
Initialization parameters removed from all pressure drop coefficients (no longer needed, since m_flow used as iteration variable; default of m_flow.start = 0 is a good guess value; a better one can be provided via a parameter)
Plan: Tests in EUROSYSLIB with larger and realistic benchmarks.

## Slide 39
Overview and Rationale for Stream Connectors - Page <number>
No special symbolic transformation algorithms needed!
Connection semantic is trivial: Generate no connection equation for stream variables
The inStream(..) operator requires to analyze all corresponding stream-variables in a connection set (e.g. with respect to "min(..)" attributes). A tool could decide to only support 1:1 connections in the beginning. The inStream(..) operator is then trivial to implement.
Inside/outside connections (= hierarchical connections) complicate issues a bit (similarly to flow-variables), but nothing serious
The tool requirements for "stream" support is very modest:

## Slide 40: 8. History and Contributors
Overview and Rationale for Stream Connectors - Page <number>
2002:ThermoPower connectors by Francesco Casella (this is the basis of the stream connector concept)
2002: First version of Modelica_Fluid that is refined until 2008. Many basic concepts are from Hilding Elmqvist. It was never possible to make the library reliable.
Jan. 2008: upstream(..) operator by Hilding Elmqvist (triggered the further development)
Jan. 2008: new formulation of "ideal mixing" from Francesco Casella (this is the basis of the inStream(..) operator)
March 2008: proposal of "stream" connectors by Rüdiger Franke
April 2008: refined proposal by Rüdiger Franke & Martin Otter, prototype in Dymola by Sven Erik Mattsson, improved definition of inside/outside connector by Hans Olsson, test of the concept by Rüdiger Franke and Michael Sielemann, reformulation to improve the numerics by M. Sielemann and M. Otter, transformation of Modelica_Fluid to streams by M. Otter
May 2008: final proposal developed by Modelica fluid group at the 57th design meeting and (positive) vote for inclusion in Modelica 3.1.
Jan 2009: Modelica_Fluid 1.0 released, based on stream connectors